## Slide 1: NEC SV9100 Startup Technical Training
2018 (Session 1)
Sales Engineering

## Slide 2: Sales SV9100 Startup Agenda
NEC Training and Certifications
NEC NTAC
Platform Overview
Licensing
SV9100 CPU Overview
System Startup (Need to Know)
Questions

## Slide 3: NEC Training and Certifications
NEC SV9100

## Slide 4: NEC Training (Sales and Technical)
https://training.necam.com/

## Slide 5: SV9100 Sales Certification Training
It is suggested that sales people and technicians take these courses.
High level overviews of the SV9100 and it’s applications
Great lead in for the technical courses
No charge classes.

## Slide 6: SV9100 Technical Certification Courses

## Slide 7: SV9100 Technical Certification Training
IP Prerequisite Course
  Exam Fee $0
SV9100 Foundation Course
  8-12 Hours
  Exam Fee $39
  SV9100 and InMail Certifications
SV9100 Foundation Courses
  Required For Technical Support

## Slide 8: SV9100 Technical Certification Training
UC Suite Certification
  4 Hours
  Exam Fee $39
InMail Certification
  4 hours
  Exam Fee $39
Advanced SIP Trunking
  4 Hours
  Exam Fee $39
SV9100 Advanced Courses (Applications)
  Required For Technical Support

## Slide 9: NEC Technical Support
NEC NTAC

## Slide 10: NEC NTAC (Technical Assistance)
https://necntac.com/
BREAK FIX!

## Slide 11: NEC NTAC (SV9100 Manuals)
SV9100 Manuals
Features and Specifications
System Hardware
PC Programming
Programming
InMail System Guide
Networking
General Description
UC Suite
Contact Center Installation
Contact Center Supervisor

## Slide 12: NEC NTAC (SV9100 Manuals)
SV9100 Manuals
Features and Specifications
System Hardware
PC Programming
Programming
InMail System Guide
Networking
General Description
UC Suite
Contact Center Installation
Contact Center Supervisor

## Slide 13: NEC SV9100
SV9100 Platform Overview

## Slide 14
SV9100S
Includes 48 System Resource Licenses
TDM
VM
UM/IP/UC Available
Upgradable…
SV9100E
Support for up to 1,296 Resources
IP included
IP/UC Focus
VM/UM
SV9100S – 48 Resources (Upgradable to E)
SV9100E – 1296 Resources
SV9100S & SV9100E

## Slide 15: SV9100S Platform
Price Focused
  IP available via IPLE
  Activate UC via User Licenses
InMail
  16 voice channels with 15 hours storage
  UM available
  8 or 16 Subscriber Mailboxes included based on package selection
48 Resource Licenses included
Maximum 48 total resources
  Expandable through migration to SV9100E
Feature set same as SV9100E

## Slide 16: SV9100E Platform
UC & IP Equipped
  IPLE included
  Embedded InMail (120 Hrs.)
  Activate UC via User Licenses
    8 or 16 User Licenses included based on package selection
UM8000 Option
  500+ hours storage
Maximum 1,296 total ports
  896 stations
  400 trunks

## Slide 17: SV9100 Chassis Types
9.5” 3 Slot Chassis (SV9100S or SV9100E)
19” 6 Slot Chassis (SV9100S or SV9100E)
SV9100 9.5” Chassis
SV9100 19” Chassis

## Slide 18
SV9100S to IP
SV9100S
SV9100S
IPLE
Need IP?
Remote Worker
48 Resources

## Slide 19: SV9100S to SV9100E (Migration Kit)
SV9100S
SV9100E
MIGRATION KIT
Migration License
Expand S to SV9100E
48 Resources
Need NetLink/More Ports?
NetLink
1296 Resources

## Slide 21
400 TRK + 896 EXT
NetLink
(IP Connection)
System Capacity
  Expandable to 1,296 total ports
  Easy to configure system capacity by adding Licenses, Chassis & Blades
Items |  |  |  | SV9100
Max Ports |  |  |  | 1,296
 | Max Trunks (Total) |  |  | 400
 |  | Analog |  | 400
 |  | ISDN |  | 400
 |  | IP |  | 400
 | Max Extensions (Total) |  |  | 896
 |  | Digital |  | 896
 |  | Analog |  | 896
 |  | IP |  | 896
 |  | Virtual |  | 512
Items |  | SV9100
InMail Hours |  | 15/120
Remote Node (NetLink) |  | 49
VoIP Channels |  | 256
ARS Tables |  | 2000
DID Tables |  | 4000
Speed Dial |  | 10,000
Phone Book |  | 110,000
Access Maps |  | 400
UC Clients |  | 256/512
Conference |  | 32x3 = 96
SV9100 Built Out

## Slide 22
Analog Station
Resources
Analog Trunk
Mobile Extension
Digital Trunk
Digital Station
IP/SIP Trunk
IP Station
Ports
Terminology

## Slide 23: NEC SV9100
SV9100 Licenses

## Slide 24: SV9100 User Licenses
Standard User License
Premium User License
(Attendant)
SV9100
Voice Mail Only License
(Digital and Analog Stations)

## Slide 25: SV9100 License Features

## Slide 26: SV9100 UC Suite License Overview
 | Feature name/description | Standard | Advanced | Premium | Ala carte
 | Standard telephony features | √ | √ | √ | 
 | Single BLF view | √ | √ | √ | 
 | Presence and Presence Profiles | √ | √ | √ | 
 | Standard Outlook Addin | √ | √ | √ | 
 | Headset mode | √ | √ | √ | 
 | Chat/Messaging | √ | √ | √ | 
 | Call history | √ | √ | √ | 
 | Contacts database | √ | √ | √ | 
 | Multi column view in BLF | √ | √ | √ | 
 | Enhanced Outlook Addin | √ | √ | √ | 
 | UC Inactivity timer | √ | √ | √ | 
Release 4.1 | Multi tab/buddy list BLF |  | √ | √ | 
 | Park Monitor |  | √ | √ | 
 | Video Call (WebRTC) |  | √ | √ | 
Release 4.5 | UC Mobile Client |  | √ | √ | 
 | Directory Edit |  |  | √ | 
 | Night Mode |  |  | √ | 
 | Phone Messaging |  |  | √ | 
 | BLF pop based on DNIS |  |  | √ | 
 | Contact Center Integration |  |  | √ | √
 | CRM license |  |  | √ | √
 | Softphone |  |  |  | √

## Slide 27: NEC SV9100 R7

## Slide 28: SV9100 R7 Ease of Installation and Maintenance
WebPro License Enhancement –
Track licenses
  Available quantity
  Quantity Used
  Remaining Licenses

## Slide 29: SV9100 R7 Ease of Installation and Maintenance
Webpro Capture Packets

## Slide 30: SV9100 R7 Ease of Installation and Maintenance
Webpro Capture Packets

## Slide 31: SV9100 R7 Ease of Installation and Maintenance
Webpro Capture Packets (Run the capture and open in Wireshark)

## Slide 32: NEC SV9100
SV9100 CPU Hardware Key Code and Licenses

## Slide 33: SV9100 CPU License Activation
The SV9100 CPU comes from the factory with no licenses on it. In order for any cards to come up and work there needs to be licenses installed.

## Slide 34: SV9100 CPU License Activation
The SV9100 CPU has a Hardware Key Code

## Slide 35: Checking The Hardware key Code and Software Level (Phone)
1. Go to any working display telephone
2. Do not lift the handset
3. Press the Feature Key and press the digit 3 on the dial pad
4. This will display the Hardware Key Code and
and software level of the CPU
5. You will register the HKC on the LMS
6. The HKC is associated with your customer and
A license file will be generated

## Slide 36: SV9100 Licensing (License File)
Once Licenses are registered to the CPU and attach the licenses is when SWA starts!
SV9100 WebPro Log In

## Slide 37: SV9100 CPU Temporary License Activation
The SV9100 CPU comes from the factory with no licenses on it. In order for any cards to come up and work there needs to be licenses installed on the CPU. For start up of a new system and adding cards after the install, you can turn on the temporary license.
The SV9100 has 3 ways to activate temporary licenses
1.) 60 Day Free License
2.) 30 Day Recovery License
3.) 0-10 Day Temporary License

## Slide 38: SV9100 60 Day Free License (Program 90-55)
60 Day Free License
The 60 Day Free License comes with the GCD-CP10. It allows for all features and all ports (except Encryption feature) to be active for 60 days.
The count down starts on the first power on and ends at midnight of the 60th day.
By default, the 60 Day Free License is set to disabled.
The 60 day count down starts when the system is initially powered on and continues if the 60 Day Free License is disabled or enabled.
The GCD-CP10 works for 1440 hours from the first time powered on.
The clock counts down only when the power supply in the chassis is ON.

## Slide 39: SV9100 Recovery License (From the LMS)
Recovery License
The recovery license turns on all licenses for up to 30 days.
To request a recovery license, go to the (LMS) License portal.
The recovery license can be used only once for each UNIVERGE SV9100 GCD-CP10.
When the System time turns to midnight of the End Date, the system resets and comes back with no free licenses.
The recovery license can be activated only from PCPro or WebPro, not a multiline terminal.

## Slide 40: SV9100 Temporary License (Program 90-37-01 = 0-10)
Temporary License
Temporary License activates all feature licenses (except the Encryption feature) and all port maximum licenses.
When the number of days for the temporary license is assigned, system reset is required for the license to take affect.
The number can be set (1~10) for 1-10 days of temporary licenses.
The Temporary License must be set from phone programming and the SV9100 has to be restarted in order for the license to start.
When the temporary license is cleared, the system reboots automatically at twelve o'clock midnight of the next day.

## Slide 41: NEC SV9100 Startup Technical Training
May 2017 (Session 1)
Sales Engineering
Charlie Setaro
Bill Kintop

## Slide 42: NEC SV9100
SV9100 CPU Overview

## Slide 43: SV9100 and the CPU
SV9100 Gateway Server
SV9100 CPU

## Slide 44
SV9100 CPU (GCD-CP10)
SV9100 CPU Components
IPLE Up To 256 IP Pad Channels
Built In Memory
InMail

## Slide 45: SV9100 InMail
9100S 1 Gig SD Card 15 hr. InMail
9100E 4 Gig SD Card 120 hr. InMail
SV9100 CPU
InMail is embedded
16 Voice Channels
15/120 Hours
960 Total Mailboxes
  896 Station Mailboxes
    32 Routing Boxes
    32 Group Boxes
SV9100 InMail Automatically Programmed!

## Slide 46: SV9100 CPU (GCD-CP10)
SV9100 CPU

## Slide 47: SV9100 CPU Overview
SV9100 CPU Connections
Ethernet Connection used for programming and applications when there is no VoIP needed. Default IP Address is 192.168.0.10
Control Relays (2) normally open can be closed by dialing a service code or pressing a function key. The relay is timer controlled. Rated at 500mA @24 VDC, 50 Ohms
AUX1 and AUX2 IN/OUT Jacks can be used for Background Music, Music on Hold or Paging Zone 9. 600 Ohm
USB Port Memory Connection (Used for upgrading software or downloading system data)
Serial Port (Used for engineering purposes only)
Load Switch which is used for initial system startup, resetting the system, or when upgrading system software
Sense Switch (Not Used)
VoIP Gigabit Port (IPLE) Used for Programming, VoIP Traffic and Applications Default IP Address 172.16.0.10
When the VOIP connection is used for IP and Applications DO NOT USE the Ethernet Port

## Slide 48: NEC SV9100
SV9100 CPU Start Up

## Slide 49: SV9100 Battery and SD Flash
SV9100 Battery
Install the battery (CR2032 3.0V coin-type lithium battery) onto the GCD-CP10.
The polarity + symbol must be on top.
The battery retains the date and time when powered off.
Install the SD Memory card
The Memory card will have an “A” for the SV9100S and a “B” for the SV9100E
The memory card stores the SV9100 Database and InMail
SDA or SDB

## Slide 50: SV9100 Defaulted System From The Factory
The SV9100 must be initialized on it’s first startup!
1.) Install the battery on the CPU
2.) Install the CPU in the first slot
3.) Press and hold the Load Button on the CPU
4.) Power the chassis on while holding the Load button
5.) Count to 10 and let go of the Load button
SLOT 1

## Slide 51: NEC SV9100
SV9100 Loading CPU Software

## Slide 52: SV9100 CPU Software Update
Always start out by initializing the CPU
Next install the latest system software
SV9100 system software can be downloaded from NTAC
Log into www.necntac.com
Set the site filter for SV9100 and Software
Search for the latest version of SV9100 software

## Slide 53: SV9100 CPU Software
Two Software File Types
  Local and Remote
  Local gets loaded using a USB stick installed on the CPU
  Remote can be uploaded locally or remotely using WebPro

## Slide 54: SV9100 Remote Software Update

## Slide 55: SV9100 Loading System Software
How to load SV9100 System Software
With power off, use a USB stick to install the SV9100 software. Make sure the file is unzipped and in the root directory. You should see seven folders and six files on your USB stick. Now insert the USB stick.
While holding the Load Switch turn power on. Hold the Load Switch for 10 seconds then release. The software will load.

## Slide 56: SV9100 Installing System Software
Loading SV9100 System Software
Wait until the Status LEDs on the GCD-CP10 have the following
indications (approximately two minutes):
LED 2: Flashing Red
LED 3: Flashing Red
LED 4: Flashing Red
LED 5: Steady Red
Turn the system power off and remove the USB Memory.

## Slide 57: Checking Software Level (Phone)
1. Go to any working display telephone
2. Do not lift the handset
3. Press the Feature Key and press the digit 3 on the dial pad
4. This will display the SV9100 CPU Software Level

## Slide 58: SV9100 WebPro Software Load
Log Into WebPro
Click on Firmware Update

## Slide 59: NEC SV9100
SV9100 Phone Programming

## Slide 60: Phone Programming
HOW TO ENTER PROGRAMMING MODE
To enter programming mode:
1. Go to any working display telephone.
2. Do not lift the handset.
3. Press Speaker.
4. Dial #*#*
5. Dial the system password 47544 + Transfer.

## Slide 61: SV9100 Terminal Keys for Entering Data (Programming Manual)

## Slide 62: NEC SV9100
SV9100 IP Connection and WebPro

## Slide 63: SV9100 CPU IP Connection
SV9100 CPU Connections
Ethernet Connection used for programming and applications when there is no VoIP needed. Default IP Address is 192.168.0.10
VoIP Gigabit Port (IPLE) Used for Programming, VoIP Traffic and Applications Default IP Address 172.16.0.10

## Slide 64: SV9100 CPU (Connection)
SV9100 CPU
VoIP Gigabit Port (IPLE)
Default IP Address 172.16.0.10
Ethernet Connection
Default IP Address is 192.168.0.10
Ethernet Connection
IP Address is 192.168.0.11
Ethernet Connection
IP Address is 172.16.0.11

## Slide 65: SV9100 Passwords (90-02 Admin. Programming Passwords)
Manufacturer Level necii 47544
Installer Level tech 12345678
Sys. Admin Level (A) ADMIN1 0000
Sys. Admin Level (B) ADMIN2 9999
User Admin Level USER1 1111

## Slide 66: SV9100 WebPro Log In
necii
47544

## Slide 67: SV9100 WebPro Log In

## Slide 68: NEC SV9100
SV9100 Installing a License File to the CPU

## Slide 69: SV9100 WebPro License File Load
Log Into WebPro
Click on Feature Activation
Click Choose File
Click Upload
Locate and Upload
The license file…

## Slide 70: NEC SV9100
SV9100 Basic Programming

## Slide 71: SV9100 Programs to Start
10-01 Time and Date
IP Information 10-12-01-09
IP Pad channels 10-54 (Should match IP License 5103)
Passwords 90-02
11-02 Extension Numbering (101-199, 201-299 Virtuals)
15-01-16
15-07 Telephone Key Programing
15-20 Names For Keys
15-25 Desi Less Page Configuration
There are 3 different types in incoming call
  Ring groups
  Direct Inward Lines (DIL)
  DID trunks